## Slide 1
Skin Cancer Diagnostics
V. P. Zakharov
Samara 2016

## Slide 2
Motivations
2

## Slide 3
Cancer Facts & Statistics (USA)
3
5 

## Slide 4
Cancer Facts & Statistics (Russia)
4
Male:
Lung cancer
Liver, stomach and esophageal cancer
Skin cancer (melanoma)
Female:
Breast cancer
Lung cancer
Gastrointestinal cancer
Skin cancer (melanoma)
Fig. – Cancer mortality-to-incidence ratio
UK
USA
RUS

## Slide 5
Skin Structure and Cancer Types
5
Melanoma (MM) ~ 5%
Keratinocyte skin cancer
  Basal cell carcinoma (BCC) ~75% (Nodular, Superficial, Morphoeic, Pigmented)
  Squamous cell carcinoma (SCC) ~20%
  Rare cancer types (Merkel cell carcinoma, Kaposi’s sarcoma T cell lymphoma) < 1%
Nevus: pigmented (PN), atypical (AN), compound (CN), intradermal (IN)

## Slide 6
Skin Cancer Statistics
6
Fig. 1 – Deaths caused by skin cancers.
Fig. 2 – Rate of melanoma in skin cancers
Fig. 3 – Increase of melanoma cases

## Slide 7
Melanoma. Clinical Presentation
7

## Slide 8
Melanoma Stages
8
Samara University

## Slide 9
Clinical Pathway
9
SFM-2016
Samara University
Visual inspection alone versus visual inspection plus dermoscopy.
Teledermatology (including clinical photographs and dermoscopic images).
Mobile phone applications.
Computer-aided diagnosis - dermoscopy-based technologies.
Computer-aided diagnosis - spectroscopy-based technologies.
Reflectance confocal microscopy.
Optical computed tomography.
Volatile organic compounds, including canine odourdetection methods.
Gene expression analysis.

## Slide 10
What instruments used?
10
Diagnostics
  Visual inspection/clinical examination
  Dermoscopy/dermatoscopy
  Spectroscopy (Diffuse, Raman scattering, fluorescence)
  Confocal microscopy
  Optical coherence tomography
  High frequency ultrasound
  Exfoliative cytology
  DNA expression analysis/Gene chip analysis
Intra-operation support/Staging
  CT
  PET
  PET-CT
  MRI
  Ultrasound +/- fine needle aspiration cytology FNAC
  Sentinel lymph node biopsy +/- high frequency ultrasound

## Slide 11
What we need?
11
1. Instrument for screening:
Aims: early skin cancer detection and differentiation;
WHO requirements: sensitivity (ideal) greater 95%,
(satisfactory) not less then 90%;
Principle characteristics:
  Fast: (ideal) real time, (satisfactory) few seconds per single diagnosis;
  Non invasive;
  No harm for patient;
  Automatic;
  Cheap.
  2. Intra-operative tool
Aims: surgery operation assessment for tumor resection boundary;
Principle characteristics:
  Fast: real time;
  3D Imaging;
  High sensitivity and specificity
  3. Post-operative control

## Slide 12
Main Diagnostic Methods
12
Histology – medical approved “gold” standard
Visual inspection
Spectral analyses
  Backscattering (BS)
  Fluorescence spectroscopy (AF)
  Raman spectroscopy (RS)
Imaging
  Confocal microscopy
  2D Imaging (RS and/or AF)
  Optical coherence tomography (3D imaging)

## Slide 13
Visual Inspection
13
Visual analysis:
ABCD -> asymmetry, border irregularity, colour variegation, diameter > 6 mm)
ABBCD -> amelanotic, bleeding, bump, colour uniformity, de novo (or “dark”)
C -> CCC -> colour, contour, and change
CD -> UC -> different, uneven, changing

## Slide 14
Visual Inspection
14
Pattern analysis:
Menzies method (presence of single colour, symmetry of pattern, blue-white veil, multiple brown dots, pseudopods, radial streaming, scar-like depigmentation, peripheral black dots or globules, multiple colours, multiple blue or grey dots, broadened network)
three point checklist (asymmetry, atypical pigment network, and blue-white structures)
seven-point dermoscopy checklist (atypical pigment network, grey-blue areas, atypical vascular pattern, radial streaming (streaks), irregular diffuse pigmentation (blotches), irregular dots and globules, regression pattern)
Notes: Pattern analysis based on colour, aspect, pigmentation pattern, and skin vessels.

## Slide 15
Screening I
15

## Slide 16
Screening II
16

## Slide 17
Principle Idea
17
Additional factors
  Haar wavelet’s coefficients (up to 3 level)
  Local Binary Pattern (LBP)
  Color Features
Color spaces
  Red-Green-Blue (RGB)
  Hue-Saturation-Value (HSV)
  CIE 1976 L*a*b or just CIELAB
  Classes differentiation
    SVM (Support Vector Machine)

## Slide 18
Personolization
18
Euclidean norm
Cosin norm
Healthy skin area
Malignant Melanoma area
{Haar, LBP, Color (RGB, HSV, LAB)} – Vector for tumor and healthy skin area
2. Difference” between tumor and healthy skin using Euclidian and cosin norm.

## Slide 19
SVM Melanoma Detection
19
Method | Experiment #1 (70 images) |  | Experiment #2 (130 images) | 
 | Sensitivity | Specificity | Sensitivity | Specificity
General | 74,3% | 62,9% | 63,1% | 80,0%
Personalized | 94,3% | 94,3% | 90,8% | 90,8%

## Slide 20
TD OCT
20

## Slide 21
Spectral Analysis
21

## Slide 22
BS
22
Maximum: sensitivity 83% and specificity 90%

## Slide 23
Spectral Analysis
23

## Slide 24
Autofluorenscence
24

## Slide 25
Autofluorenscence
25

## Slide 26
Autofluorenscence
26
No | Comparison | Accuracy
1 | Sound skin/Compound nevus | 91,1 %
2 | Compound nevus/Displastic nevus | 69,6 %
3 | Displastic nevus/Malignant melanoma | 74,1 %
4 | Sound skin/ Base cellular papyloma | 87,5 %
5 | Sound skin/ Base cellular carcinoma | 82,2 %
6 | Base cellular papyloma/Base cellular carcinoma | 92,6 %
Borisova E. et.al., Institute of Electronics, Bulgaria

## Slide 27
RS
27

## Slide 28
Autofluorenscence
28

## Slide 29
Experimental Setup
29

## Slide 30
FD OCT
30

## Slide 31
OCT
31
OCT images of BCC (a) and MM (b), 1.5 × 1.5 mm each (arrows indicate tumorous areas in healthy skin) and corresponding histologic section of BCC (c), and MM (d), ×100 magnification.

## Slide 32
RS
32
Raman scatterer | Raman band, cm-1
stretching mode C = N | 1240 - 1280
twisting, wagging of bending mode CH2 | 1300 - 1340
CH2 deformations of proteins and lipids | 1440 - 1460
stretching mode C = O in amide I | 1640 - 1680

## Slide 33
RS-AF. Restrictions
33
*Chetan A. Patil,* Isaac J. Pence, Chad A. Lieber, and Anita Mahadevan-Jansen
January 15, 2014 / Vol. 39, No. 2 / OPTICS LETTERS

## Slide 34
RS-AF. Restrictions
34
Representative Raman spectral differences that can be obtained from a single sample acquired using two different probes. (A) A conventional filtered Raman probe (green) and a beam-steered Raman probe (blue) on skin in vivo demonstrate unique line shapes. (B) Two iterations of the same probe design used to measure an albumin sample demonstrate the effect of slightly different inline filters on the raw and resulting processed (inset) Raman spectrum.

## Slide 35
RS-AF. Restrictions
35
Impact of background elimination varies based on the sample or tissue measured. Fluorescence subtraction using (A) 5th order polynomial in skin and cervix yield unique shapes due to compositional differences. (B) Using a 5th versus 7th order polynomial in colon (processed spectra inset) demonstrates that a single polynomial fitting order may not be appropriate for all samples; higher order polynomials are used to simulate background fluorescence and subtracted to enhance the underlying Raman signal from the sample.

## Slide 36
Skin Cancer Diagnostic Accuracy
36
Disease | Accuracy | OCT | RS | BS | RS-OCT | RS-BS-OCT
MM | sensitivity, % | – | 89 | 82 | 89 | 89
 | specificity, % | – | 88 | 93 | 88 | 93
BCC | sensitivity, % | 78 | 78 | 89 | 89 | 100
 | specificity, % | 96 | 85 | 80 | 96 | 96
Any skin tumor (Mean values) | sensitivity, % | 39 | 84 | 86 | 89 | 95
 | specificity, % | 48 | 87 | 87 | 92 | 95

## Slide 37
NIR AF
37

## Slide 38
VIS AF
38
Excitation spectra
Emission spectra
Fluorophore | Excitation, nm | Emission, nm
Lipo-pigments | 350, 430 | 570
Protoporphyrin IX | 408,538,506,580 | 635,700
Zn-Protoporphyrin IX | 418,550 | 588,638
Flavins | 450 | 535

## Slide 39
VIS FI
39
Fluorophore | Excitation, nm | Emission, nm
Lipo-pigments | 350, 430 | 570
Protoporphyrin IX | 408,538,506,580 | 635,700
Zn-Protoporphyrin IX | 418,550 | 588,638
Flavins | 450 | 535
Fig. 9 – Autofluorescence spectra of skin tissues

## Slide 40
RS-AF
40
Multidimensional “biochemical” tumor identification:
  RS – 4 spectral criteria, correlated with alteration of amid 1, protein and lipid content;
  NIR AF – 2 spectral criteria, correlated with alteration of melanin content;
  VIS AF – 4 spectral criteria, correlated with alteration of flavins and porphirins content.

## Slide 41
PCA Analysis
41
SFM-2016
Samara University
MM and BCC classification using multidimentional spectral criteria space

## Slide 42
MM vs BCC
42
Method of analysis | Sensitivity | Specificity | Accuracy
RS | 97.4% | 62.2% | 80.3%
NIR AF | 92.3% | 37.5% | 64.6%
VIS AF | 80% | 77.8% | 78.4%
VIS AF + NIR AF | 70% | 92.6% | 86.5%
RS+ NIR AF | 94.9% | 92.5% | 93.7%
RS+ NIR AF + + VIS AF | 100% | 96.3% | 97.3%

## Slide 43
BS+Flur+RS
43
Liang Lim et al, University of Texas

## Slide 44
Fluorenscence Imaging
44
indocyanine green (ICG)
folate-fluorescein (EC-17)
Ryan P. Judy et.al, University of Pennsylvania, USA

## Slide 45
RS-AF. Enhacements
45
Raman imaging - measuring Raman spectra through point or line scanning of the excitation and collection beams (long integration times necessary to acquire a Raman image successfully);
RS high-wavenumber, generally 2200–4500 cm−1 where distinct and strong features of lipids, proteins and water may be observed (Such signal is inherently and require different gratings, filters and more importantly detectors in order to efficiently collect signals);
Spatially offset Raman spectroscopy (SORS): Photons that undergo many scattering events are more likely to undergo a larger transverse shift and also travel deeper within the tissue (SORS better suited for low-resolution depth-dependent measurement of features and at greater depths (~centimeters) than confocal Raman spectroscopy);
Surface enhanced Raman spectroscopy (SERS): Raman effect greatly strengthened if single molecules are attached to metal nanoparticles of a suitable material and roughness to capitalize on both electromagnetic (surface plasmon resonance) and chemical enhancement.

## Slide 46
AF + RS
46
      Sinyoung Jeong & Yong-il Kim, Seoul National University, Republic of Korea

## Slide 47
OCT+RS
47

## Slide 48
HIS Setup
48
1 – broadband LED source; 2 – object;
3 – backscattered radiation; 4 – collimator;
5 – tunable monochromator; 6 – lens;
7 – digital camera; 8 – computer;
9, 11,13 – polarizers; 10,12 – acousto-optic cells;
14 – controller; 15,16 – HF amplifiers;
17 – HF generator

## Slide 49
Hyperspectral Imaging (HIS)
49
1
0
0.8
0.6
0.4
0.2
a
b
d
c
1
0
0.8
0.6
0.4
0.2
a, b – malignant melanoma;
c, d – pigmented nevi

## Slide 50
Conclusions
50
Skin cancer diagnostic tools future: multimodal approach combining morphological (imaging) and biochemical (spectroscopy technique) information.
The highest accuracy for skin cancer classification (with sensitivity and specificity greater then 90%) may be achieved by simultaneous usage of autofluorenscence and Raman spectroscopy, which based on different native biochemical markers.
HSI-RS-AF may be one of the best candidates for fast and sensitive diagnostic tool for mass screening
OCT-RS-AF may serve as universal tool for early diagnostic and intra-operative support with high accuracy (> 95%) and cellular resolution.

## Slide 51
По желанию – личные контактные
данные автора,
телефон,
e-mail